Kontalk client/server protocol
Revision 1

# Protocol overview
The Kontalk protocol operates entirely on HTTP GET or POST requests. No other method should be used in order to maintain portability and access even for users behind proxies and similar.
A Kontalk server is seen by a client using its base URL – we will take the Kontalk main server as an example:
http://www.kontalk.net/messenger

Starting from this URL, various server functions can be called. Almost every command is issued mainly by appending parts to the base URL (e.g. path parts and parameters), except for some commands which require a request body after the HTTP headers (e.g. sending messages).
All the response bodies of the Kontalk server are sent using Google Protocol Buffers (http://code.google.com/apis/protocolbuffers/), serialized on the channel and sent as raw data, using the content type application/x-google-protobuf.
As for the request bodies, some of them are raw data (e.g. messages to be sent), others are packaged using protocol buffers, like responses. All of that will be explained in detail later in this document.
# User registration and authentication
## User registration
User registration is done using a two-way verification process. In the first step, the client sends to the server the user's phone number. The server then sends a message to that number (presumably on the same device) with a validation code.
The client catches that code and sends it to the server, proving that the phone number is real and owned by the actual user who is trying to register.
If the servers verifies that the validation code is correct, it generates a user authentication token and sends it to the client. The token is a special string that is passed over in all subsequent requests to the server – it uniquely identifies a user/device pair (this allows multiple devices to be registered with the same phone number – e.g. a phone with a SIM card and a tablet without SIM card).

## Authentication
In any case – if requested by the specific command – any HTTP request to the server must be accompanied by the user authentication token received during the registration process. This must be passed using the Authorization header:
Authorization: KontalkToken auth=[token]

where [token] is the user authentication token. Not passing that header will result in a 403 Forbidden HTTP error code.
Note that not all commands need authentication (e.g. requesting information about the server is a public command).
# The endpoints
The “endpoints” can be interpreted as commands sent to the server. There are several endpoints for a Kontalk server, each serving a different purpose:
- validation
- authentication
- serverinfo
- received
- message
- lookup
- polling
- download
- update
- serverlist

A client can use an endpoint simply by appending its name to the base server URL:
http://www.kontalk.net/messenger/validation
## validation
The validation endpoint is used to send a user's phone number to the server so that it can be verified. The syntax is really simple:
http://www.kontalk.net/messenger/validation/[number]

where [number] is the URL-encoded phone number – including the international prefix in the form +NN.
The response is defined messages.proto:
message PhoneValidation {
    required Status status = 1;
    optional string sms_from = 2;
}

The status field is the result of the validation; The sms_from field is optional and can contain the phone number from which the validation SMS would be sent – this is useful to the client to catch the right incoming SMS.